## Slide 1: Differentiable Programming for Modeling and Control of Energy Systems
Ján Drgoňa Collaborators: Aaron Tuor, James Koch, Shrirang Abhyankar, Ethan King, Wenceslao Shaw Cortez, Soumya Vasisht, Sayak Mukherjee, Mahantesh Halappanavar, Draguna Vrabie
American Control Conference 2023, San Diego

## Slide 2: Challenges of Dynamical Systems Modeling and Control
Simulations are crucial for many areas of decision-making and scientific discovery
Need: Improve computational efficiency and scalability for heterogenous scientific simulations
Challenges:
  Data-driven predictive modeling and verification
  Simulation of complex multi-scale systems of systems
  Optimal control and design of complex systems
Emerging solution:
  Scientific Machine Learning connecting physics and AI domains

## Slide 3: Landscape of Solution Methods
Constrained optimization
Differential equations
Supervised Learning
Requires prior knowledge of objective function and constraints
Requires prior knowledge of the physics to be modeled
Requires large labeled datasets
Reinforcement Learning
Requires environment model to sample
More domain knowledge
Less domain knowledge

## Slide 4: Landscape of Solution Tools
Constrained optimization
Differential Equations
Supervised Learning
Reinforcement Learning
More domain knowledge
Less domain knowledge

## Slide 5: Landscape of Solution Tools
Online optimization
Differential Equations
Supervised Learning
Reinforcement Learning
What comes next? … Differentiable programming (DP): a unifying approach for data-driven modeling and optimization of complex systems based on automatic differentiation (AD)

## Slide 6: Differentiable Programming Enables Scientific Machine Learning
Differentiable Programming
  M. Innes, et al., A Differentiable Programming System to Bridge Machine Learning and Scientific Computing, 2019
Physics-informed Neural Networks
  M. Raissi, et al., Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations, 2019
Neural Differential Equations
  R. T. Q. Chen, et al., Neural Ordinary Differential Equations, 2019
  C. Rackauckas , et al., Universal Differential Equations for Scientific Machine Learning, 2021
Differentiable Optimization
  A. Agrawal, et al., Differentiable Convex Optimization Layers, 2019
  P. Donti, et al., DC3: A learning method for optimization with hard constraints, 2021
  S. Gould, et al., Deep Declarative Networks: A New Hope, 2020
  J. Kotary, et al., End-to-End Constrained Optimization Learning: A Survey, 2021
Differentiable Control
  B. Amos, et al., Differentiable MPC for End-to-end Planning and Control, 2019
  S. East, et al., Infinite-Horizon Differentiable Model Predictive Control, 2020

## Slide 7: NeuroMANCER: a Scientific Machine Learning Library
import neuromancer as nm
p = nm.constraints.variable(‘p’)
x = nm.constraints.variable(‘x’)
y = nm.constraints.variable('y’)
obj = ((1-x)**2 + p*(y-x**2)**2).minimize(weight=1.0, name='obj’) c1 = (p/2)**2 <= x**2 + y**2
c2 = x**2 + y**2 <= p**2
c3 = x >= y net = nm.blocks.MLP(insize=2, outsize=2, hsizes=[80]*4) map = nm.maps.Map(net, input_keys=['p’], output_keys=[‘x’,‘y’])
loss = nm.loss.PenaltyLoss([obj], [c1, c2, c3]) problem = nm.problem.Problem([map], loss)
optimizer = torch.optim.AdamW(problem.parameters()) trainer = nm.Trainer(problem,data,optimizer)
best_model = trainer.train()
2. Python code interface
1. Mathematical formulation
4. Results
3. Problem graph
map

## Slide 8: Data-driven Modeling Capabilities in Neuromancer
Graph Neural Networks
Component-based Physics-informed Machine Learning
Networked Dynamical systems
Differential Equation Solvers

## Slide 9: Networked Dynamical Systems via Universal Differential Equations
Network of unknown oscillators
Coupling adjacency
Ground truth Kuramoto system:
Generalization of learned dynamics on never-seen network topology.
  James Koch, et al., Structural Inference of Networked Dynamical Systems with Universal Differential Equations, Chaos: An interdisciplinary Journal of Nonlinear Science, doi.org/10.1063/5.0109093, 2023

## Slide 10: Optimal Control Capabilities in Neuromancer
Learning stabilizing controllers
Trajectory optimization and obstacle avoidance
Code generation and edge deployment – under development

## Slide 11: Differentiable Predictive Control (DPC)
From data to optimized explicit predictive control policy
  Online optimization
  Optimize for control actions
  Implicit solver-based control policy
  Offline optimization
  Optimize for control policy parameters
  Explicit neural control policy
MPC
DPC
Cost:
Model:
Constraints:
Jan Drgona, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, Journal of Process Control, 2022

## Slide 12: Differentiable Predictive Control (DPC)
Learning-based control using differentiable system models
Jan Drgona, et al., Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning, Journal of Process Control, 2022
  Optimization over design parameters representing different scenarios
  Differentiable system model allows for counterfactual reasoning based on forward simulations
  Evaluate quality of the soliton based on domain specific metrics

## Slide 13: Learning Stable Policies with Neural Lyapunov Functions
Sayak Mukherjee, Ján Drgoňa, Aaron Tuor, Mahantesh Halappanavar, Draguna Vrabie, Neural Lyapunov Differentiable Predictive Control, Conference on Decision and Control (CDC), 2022

## Slide 14: Learning Safe Policies with Control Barrier Functions
Wenceslao Shaw Cortez, et al., Differentiable Predictive Control with Safety Guarantees: A Control Barrier Function Approach, Conference on Decision and Control (CDC), 2022

## Slide 15: Economic Differentiable Predictive Control of Building Energy System
  Jan Drgona, Aaron Tuor, Elliott Skomski, Soumya Vasisht, Draguna Vrabie, Deep Learning Explicit Differentiable Predictive Control Laws for Buildings, IFAC NMPC 2021
Architectures
Neural state space dynamics model
MLP control policy architecture
Results
Multi-input multi-output system dynamics
Dynamic economic control objective
Parametric constraints

## Slide 16: Dynamics-Aware Economic Redispatch via Differentiable Predictive Control
Results
5 orders of magnitude speed-up
Near optimal performance
Ethan King, Ján Drgoňa, Aaron Tuor, Shrirang Abhyankar, Craig Bakker, Arnab Bhattacharya, Draguna Vrabie, Koopman-based Differentiable Predictive Control for the Dynamics-Aware Economic Dispatch Problem, 2022 American Control Conference
Problem: Current redispatch processes do not incorporate system dynamics concerns. Incorporating dynamics in redispatch is too complex and/or time-consuming
Solution: Machine-learning based dynamics-aware redispatch. Learn system dynamics and control policies for faster assessment.
Architectures
Koopman dynamics model
CNN control policy

## Slide 17: Edge Deployment of Differentiable Predictive Control
Flexy-Air system sketch with Raspberry-Pi controller
  Jan Drgona, Karol Kis, Aaron Tuor, Draguna Vrabie, Martin Klauco, Differentiable Predictive Control: An MPC Alternative for Unknown Nonlinear Systems using Constrained Deep Learning; Journal of Process Control, 2022
Proof of concept for AI on the edge platform.

## Slide 18: NeuroMANCER
Open-source scientific machine learning (SciML) toolbox in PyTorch for integrating deep learning, constrained optimization, and physics-based modeling
Physics-informed machine learning
Data-driven modeling of dynamical systems
Model-based policy optimization
Parametric constrained optimization
github.com/pnnl/neuromancer

## Slide 19: Acknowledgements
James Koch
Zhao Chen
Stefan Dernbach
Draguna Vrabie
Aaron Tuor
Ethan King
Christian M. Legaard
Soumya Vasisht
Wenceslao Shaw Cortez
Sayak Mukherjee
Mahantesh Halappanavar
Shrirang Abhyankar